## Slide 1: Argon ISA
ISA decoding

## Slide 2: ALU Instructions
31
30 -- 28
I – flag (if set, this command is immediate, next one is 32 bit data );
I-type commands don’t use R2 field;
27 -- 24
1
3
4
Full op code (3 bit for pipe id and 4 for real op code)
For ALU instructions 30—28 bits are equal to “000”
23 -- 20
19 -- 17
16 -- 13
4
4
4
10-5
6
4-0
4
R0 R1 R2 not used cond flags
12
11
S – signed flag; if set operation is signed
CF – change flags; if set, operation change flags
1
1
i, a, or, R2, R0, R0 // r2 := (r0 | 2)
di, 2 // data that is equal to 2
r, a, add, R0, R1, R2 // r0 := r1 + r2
8

## Slide 3: MEM Instructions
31
30 -- 28
I – flag (if set, this command is immediate, next one is 32 bit data );
I-type commands don’t use R2 and ‘mem offset’ fields;
R-type commands use ‘mem offset’ field;
27 -- 24
1
4
23 -- 20
19 -- 17
16 -- 13
4
4
4
12 -- 5
8
4-0
4
R0 R1 R2 mem offset [0-255] cond. flags
r, m, sw, RX, R3, R2, 255 // mem(r2+255) := r3 // RX is not used! set to R0;
r, m, lw, R0, RX, R2, 255 // r0 := mem(r2+255) // RX is not used! set to R0;
//
i, m, sw, R0, R3, R2, 255 // mem(r2+1024) := r3  ‘255’ is ignored
di, 1024
3
Full op code (3 bit for pipe id and 4 for real op code)
For ALU instructions 30—28 bits are equal to “000”