## Slide 1: Argon CPU bypassing
There are totally 5 bypass ways
(but only 4 are used)

## Slide 2: 1) After X to D
F D X M W
add R3,R2,R1 | F D X M W
nop | F D X M W
add R4,R3,R1 | F D X M W

## Slide 3: 2) After M to D
F D X M W
add R3,R2,R1 | F D X M W
nop | F D X M W
nop | F D X M W
add R4,R3,R1 | F D X M W

## Slide 4: 3) After X to X
F D X M W
add R3,R2,R1 | F D X M W
add R4,R3,R1 | F D X M W

## Slide 5: 4) After M to X
F D X M W
lw R3, (R2+255) | F D X M W
nop | F D X M W // (auto stall)
add R4,R3,R1 | F D X M W

## Slide 6: 5) After M to M
F D X M W
lw R3,(R2+255) | F D X M W
lw R4,(R3+255) | F D X M W
Don’t do this, because memory instructions are of 2 cycles latency